## Slide 1
EMBEDDED SYSTEMS — STM32F746G-DISCOVERY
Touchscreen Control Panel
A bare-metal touch UI for LED and servo control, built on the STM32F7 HAL
STM32CubeIDE | HAL Drivers | C
1

## Slide 2
PROJECT OVERVIEW
What this firmware does
• Bare-metal C application for the STM32F746G-Discovery board (Cortex-M7 @ 216 MHz), built with STM32CubeIDE and the STM32F7 HAL/BSP layers.
• 480×272 capacitive touch LCD driven by LTDC + DMA2D, with an FT5336 touch controller over I2C for finger input.
• Single main loop, three pages: a Home menu, an LED control page, and a Servo control page, switched via on-screen touch buttons.
• Each page follows the same pattern: Init() sets up state, Process() reads touch input, UpdateState() redraws only what changed — avoiding full-screen flicker.
2

## Slide 3
ARCHITECTURE
Navigation & shared modules
PAGE_HOME
Landing menu
routes to LED / Servo pages
PAGE_LED
led_touch_button.c
touch-toggled GPIO outputs
PAGE_SERVO
servo.c
manual slider + auto sweep
• touch_button.c / .h — shared TS_Button type: drawButton(), isButtonPressed(), and the new getTouchPosition() for continuous drag tracking.
• Dirty-flag redraw — each page only repaints elements whose on-screen value actually changed since the last loop tick.
• main.c owns the AppPage state machine and dispatches Init/Process/UpdateState for the active page each loop.
3

## Slide 4
FEATURE
LED Control Page
• Touch buttons toggle GPIO-driven LEDs on and off.
• Uses the same TS_Button + isButtonPressed() abstraction as every other page.
• Button state is redrawn only on change, keeping the touch loop responsive.
LED 1
LED 2
LED 3
4

## Slide 5
FEATURE — HEADLINE REDESIGN
Servo Control: Manual Mode
• Volume-fader style slider replaces the old +10° / –10° tap buttons.
• Drag anywhere near the rail and the knob follows your finger continuously — no separate step buttons.
• Live angle readout printed inside the knob itself (0–180°).
• Colored fill below the knob shows the current level, gray rail above it, matching classic fader UI conventions.
• AUTO mode grays it out and sweeps the angle automatically — the slider becomes read-only feedback.
95°
5

## Slide 6
IMPLEMENTATION
Servo control — under the hood
• TIM2 PWM, channel 1 drives the servo; pulse width is linearly mapped from 500–2500 µs onto the 0–180° range.
• getTouchPosition(x, y) new helper added to touch_button.c — returns the raw touch point so the slider can track drags, not just discrete taps.
• Slider redraw strategy: erase the full slider column → redraw gray rail → redraw colored fill → redraw knob → redraw angle text. Simpler and glitch-free vs. tracking partial dirty rectangles for a value that moves every frame.
• AUTO sweep steps the angle by 2° every 20 ms between 0‑80°, reversing direction at each limit.
6

## Slide 7
BUILD SYSTEM
Fixing a broken link: missing Reset_Handler
• Symptom: linker warning “cannot find entry symbol Reset_Handler; defaulting to 08000000” after an incremental build.
• Root cause: Debug/objects.list (STM32CubeIDE's auto-generated linker input list) was stale — it was missing entire folders: Core/Src, Drivers/STM32F7xx_HAL_Driver, and the startup object. The linker “succeeded” while silently omitting almost the whole application.
FIX
Project → Clean… (select the project, “Start a build immediately”) forces CubeIDE
to regenerate every subdir.mk / objects.list from the current source tree, then fully
recompiles and relinks — a plain incremental build will not repair this on its own.
7

## Slide 8
TECH STACK
Hardware & toolchain
MCU
STM32F746NGH6 — Cortex-M7 @ 216 MHz
Display
4.3" 480×272 RGB565 LCD via LTDC + DMA2D
Touch
FT5336 capacitive touch controller over I2C
Servo PWM
TIM2 channel 1, 500–2500 µs pulse → 0–180°
Toolchain
arm-none-eabi-gcc via STM32CubeIDE, STM32F7 HAL/BSP
8

## Slide 9
ROADMAP
Possible next steps
• Add decorative tick marks along the slider rail for closer visual fidelity to the fader reference design.
• Persist last servo angle / mode across power cycles (e.g. via EEPROM on the Discovery board).
• Extend the page pattern to a new sensor or camera page using the same Init/Process/UpdateState convention.
• Add on-target verification: flash after each change and confirm touch response and colors on real hardware.
9

## Slide 10
Thank you
STM32F746G-Discovery Touch Display Project
10